## Slide 1: Frameworks Integration
KS, 5/14/2012

## Slide 2: Existing Test Framework (“Cupertino Lab”)
Driver
DUT
ADB
Target
AP
AP
AP
KATS
Cisco
Enterprise
AP
Corporate network
Test network
WiFi link
Serial link

## Slide 3: Cupertino Lab (cont’ed)
For Cisco Enterprise APs
  AP can be dynamically configured through serial link
  Access through Serial Console and Pexpect
For all other consumer class APs
  Use the same Serial Console as a stub (no on-the-fly configuration)
  Assume the AP has been pre-configured as stated

## Slide 4: Proposed Integration with the WiFi Test Farm (“FARM”)
Driver
DUT
ADB
Farm-Target
AP
AP
AP
KATS
Cisco
Enterprise
AP
Corporate network
Test network
WiFi link
Serial link
New

## Slide 5: Goals
Make consumer class APs available to Cupertino Lab’s existing test framework
Make consumer class APs dynamically configurable
Reuse all existing test cases (100+, for tablet)
Meet KATS integration requirements

## Slide 6: High-level Requirements
FARM-TARGET should provide a serial link access
This link could be virtual - when DRIVER and FARM-TARGET is the same machine
This link should present a CLI interface
A CLI/Client Python class should integrate with the existing Serial Console class on DRIVER
A CLI/Server should integrate with FARM-TARGET’s existing Dynamic AP Configuration Service

## Slide 7: High-level Design
Existing
Test Suites
Serial Console /
PExpect
CLI
Client Class
Transport
CLI
Server App
Transport
Dynamic AP
Configuration Service
AP
New Components
DRIVER
FARM-TARGET

## Slide 8: Next Steps
Neusoft: Send engineers over to work with Glen’s team, get familiar with the existing framework
Go through the design cycle of the new CLI interface
Discuss DB requirements for this integration