## Slide 1: WiFi Training
KS, 5/21/2012

## Slide 2: Topics
The View from 30,000 feet
Joining a Network
MAC Frames – Session 1
AirPcap – Session 1
MAC Frames – Session 2
AirPcap – Session 2
MAC Frames – Session 3
Security
PHY
RF
Case Studies

## Slide 3: The View from 30,000 feet

## Slide 4: Overview
Wireless LAN in real world
Standards & Technologies
Protocol Map
Differences between wired and wireless
Common problems

## Slide 5: WLAN in Real World
“Ethernet is dead” (2012)
“Wireless networks are an excellent complement to fixed networks” (2005)

## Slide 6: Standards
Relationship with 802
Relationship with 802.3

## Slide 7: Standards
Timeline: http://grouper.ieee.org/groups/802/11/Reports/802.11_Timelines.htm
802.11-2007
  802.11a-1999: 5 GHz, 54 Mbps
  802.11b-1999: 2.4 GHz, 11 Mbps
  802.11g-2003: 2.4 GHz, 54 Mbps
802.11n-2009: 2.4/5 GHz, N*150 Mbps

## Slide 8: More Standards
802.11i: Security
802.11h: Spectrum & TX power management
802.11e: QoS
802.11d: International roaming
and more …

## Slide 9: 802.11n Technologies
OFDM – multiple subcarriers
MIMO – multiple spatial streams
HT-40 – 2x20 MHz channel width
Others
  Aggregation
  BlockACK

## Slide 10: Protocol Map

## Slide 11: Wireless vs. Wired
Need a connection process
Half-duplex
High error rate, so retransmission is required
Channel capacity is shared by everyone
Can be easily sniffed, jammed, cracked, …
High power consumption
Lower throughput

## Slide 12: Common Complaints
“Which AP? What is the password?”
“I can’t connect …”
“The connection is not stable …”
“My network is SLOW …”
“Skype quality is really bad …”
“Battery couldn’t last overnight …”
“… I still can’t connect …”

## Slide 13: Joining a network

## Slide 15: What’s in a Network?
Other Stations
APs
Bridging service
Distribution System

## Slide 16: Re-joining a Network
Basic Service Set (BSS)
Extended Service Set (ESS)
SSID

## Slide 17: MAC frames – session 1

## Slide 18: General Frame Format
Optional

## Slide 19: Frame Control Field
b3 b2 | Type
00 | Management
01 | Control
10 | Data

## Slide 20: Watch Out for the Bit-Ordering !
Standards documents use
  Little-Endian in diagrams
  Big-Endian in descriptions
Wireshark
  Always uses big-Endian

## Slide 21: 3 Types of MAC Frames
Management frames
  Beacon, Probe Request, Probe Response, …
  Association, Disassociation, …
Data frames
Control frames
  ACK, …

## Slide 22
Data
Data

## Slide 23: Management Frame

## Slide 24: Management Frame – 802.11n

## Slide 25: Mgmt Frame Body Components
Fields
  Fixed length
  Fixed order
Information Elements (IE)
  Variable length
  Relative order

## Slide 26: Example: Beacon
Fixed fields
  Timestamp (8-byte)
  Beacon Interval (2-byte)
  Capability (2-byte)
IE’s
  SSID
  Supported Rates
  TIM
  …

## Slide 27: Data Frame

## Slide 28: Data Frame – 802.11n

## Slide 29: Data Frame with No Data
“Null Function”
Used for
  Keep alive
  Notify power save condition

## Slide 30: Control Frame - ACK

## Slide 31: Control Frame - BlockAck

## Slide 32: Airpcap – session 1

## Slide 33: AirPcap – Wireless Sniffer
Capture – select interface and channel
Display filter

## Slide 34: Problems with Wireless Sniffing
You (the sniffer) may not be able to hear it
You may not be able to hear it correctly
You may not hear all of the packets
Replace “you” with “they (receivers)”

## Slide 35: Interface & Channel

## Slide 36: Packet Capture
Live exercises
Scan, connect, ping & suspend –

## Slide 37: Display Filter
We are only interested in packets within our network
wlan.bssid == 2c:b0:5d:46:a8:bb

## Slide 38: Which BSSID?
root@android:/ # wpa_cli status
Using interface ‘wlan0’
bssid=2c:b0:5d:46:a8:bb
ssid=ksap-2g
id=1
mode=station
pairwise_cipher=NONE
group_cipher=NONE
key_mgmt=NONE
wpa_state=COMPLETED
ip_address=192.168.2.111
address=28:ef:01:0e:af:b7

## Slide 39: Display Filter
We are only interested in packets within our network
Management frames only
(wlan.bssid == 2c:b0:5d:46:a8:bb) && (wlan.fc.type == 0x0)

## Slide 40: Display Filter
We are only interested in packets within our network
Management frames only
But do not include Beacons
(wlan.bssid == 2c:b0:5d:46:a8:bb) && (wlan.fc.type == 0x0) && (wlan.fc.type_subtype != 0x8)

## Slide 41: Mac frames – session 2

## Slide 42: Management Frames
Beacons, BSSID
Probe request, response
Association
Disassociation

## Slide 43: Management Frame – 802.11n
HT Control: optional

## Slide 44: Beacon

## Slide 45: What to look for in Beacon?
BSSID
Capabilities Information
SSID
RSN
TIM and DTIM
HT Capabilities
HT Information

## Slide 46: Authentication Request

## Slide 47: Authentication Response

## Slide 48: Association Request

## Slide 49: What to look for in Assoc Req?
BSSID
Capabilities Information
SSID
RSN Information

## Slide 50: Association Response

## Slide 51: What to look for in Assoc Resp?
Status code
Association ID

## Slide 52: Data Frame – 802.11n

## Slide 53: Data

## Slide 54: What to look for in Data?
Frame Control/Flags
  To or from DS?
  Retry?
Sequence number
FCS

## Slide 55: Control Frame - ACK

## Slide 56: What to look for in ACK?
Receiver Address

## Slide 57: Airpcap – session 2

## Slide 58: AirPcap – Session 2
Display filter macro
Capture filter
Sniffing 40 MHz channel with AirPcap

## Slide 59: Display Filter Macros

## Slide 60: Display Filter Macros
Macro name : definition
(wlan.bssid == 2c:b0:5d:46:a8:bb)
my_bssid
(wlan.fc.type_subtype == 0x08)
beacon
(wlan.fc.type == 0x00)
mgmt

## Slide 61: Display Filter Using Macros
We are only interested in packets within our network
Management frames only
But do not include Beacons
${my_bssid} &&
${mgmt} &&
!${beacon}

## Slide 62: Saved Filters and Macros

## Slide 63: Capture Filter
Wireshark / TShark
libwiretap
dumpcap
WinPcap / libpcap
libwireshark
Live data
Capture file
libwiretap
Display filters
Plugins
Dissectors
Tree

## Slide 64: Capture Filter
We are only interested in packets between the AP and us
But something is missing …
(wlan host 2c:b0:5d:46:a8:ba) ||
(wlan host 28:ef:01:0e:af:b7)
Notes: http://www.lovemytool.com/blog/2010/07/wireshark-wireless-display-and-capture-filters-samples-part-2-by-joke-snelders.html

## Slide 65
BPF: “wlan host 2c:b0:5d:46:a8:ba”
Compiled BPF:
(000) ldb [3]
(001) lsh #8
(002) tax
(003) ldb [2]
(004) or x
(005) st M[0]
(006) tax
(007) ldb [x + 0]
(008) jset #0x4 jt 40 jf 9
(009) jset #0x8 jt 10 jf 31
(010) ldb [x + 1]
(011) jset #0x2 jt 12 jf 21
(012) jset #0x1 jt 13 jf 17
(013) ld [x + 26]
(014) jeq #0x5d46a8ba jt 15 jf 27
(015) ldh [x + 24]
(016) jeq #0x2cb0 jt 39 jf 27
(017) ld [x + 18]
(018) jeq #0x5d46a8ba jt 19 jf 35
(019) ldh [x + 16]
(020) jeq #0x2cb0 jt 39 jf 35
(021) ld [x + 12]
(022) jeq #0x5d46a8ba jt 23 jf 25
(023) ldh [x + 10]
(024) jeq #0x2cb0 jt 39 jf 25
(025) ldb [x + 1]
(026) jset #0x1 jt 27 jf 35
(027) ld [x + 18]
(028) jeq #0x5d46a8ba jt 29 jf 40
(029) ldh [x + 16]
(030) jeq #0x2cb0 jt 39 jf 40
(031) ld [x + 12]
(032) jeq #0x5d46a8ba jt 33 jf 35
(033) ldh [x + 10]
(034) jeq #0x2cb0 jt 39 jf 35
(035) ld [x + 6]
(036) jeq #0x5d46a8ba jt 37 jf 40
(037) ldh [x + 4]
(038) jeq #0x2cb0 jt 39 jf 40
(039) ret #65535 // Accept
(040) ret #0 // Ignore
jset: bit-wise AND
[x + 0]: first byte of 802.11 MAC frame
(008) says: If this is a Control frame (b2 == 1), ignore it (jt 40)

## Slide 66: Sniffing 40 MHz Channel
There seem to be some problems with AirPcap at 40 MHz channel
Limited success:
AP channel | 36 | 40
wl status: channel spec | 38 (40 MHz) | 38 (40 MHz)
control channel | 36 | 40
Wireshark channel | 36 | 36
Wireshark channel offset | +1 | +1

## Slide 67: Mac frames – session 3

## Slide 68: MAC Frames (3)
Unicast, multicast, broadcast
ACK, Block-ACK
Power management

## Slide 69: Unicast, Multicast & Broadcast
Unicast requires acknowledgement
Multicast & Broadcast can not be acknowledged

## Slide 70: ACK
Why is there no sequence number?
Why is there no source address?

## Slide 71: Block ACK Operations

## Slide 72: Control Frame - BlockAck

## Slide 73: ADDBA Request
Notes: 5G_udp_rx_blockACK.pcap

## Slide 74: ADDBA Response
Notes: 5G_udp_rx_blockACK.pcap

## Slide 75: Block-ACK
Notes: 5G_udp_rx_blockACK.pcap

## Slide 76: Power Mgmt – Entering PS Mode

## Slide 77: Power Mgmt – Waking Up

## Slide 78: Security

## Slide 79: PSK

## Slide 80: PTK

## Slide 81: Message 1
Notes: Wpa2_2.4G-scan-connect-ping-suspend.pcap; Use display filter “eapol”.

## Slide 83: Encryption

## Slide 84: Encrypted Data Frame
This is a PING reply.
So, why did the display filter “ip” and “icmp” fail?
Notes: wpa2_2.4G-scan-connect-ping-suspend.pcap

## Slide 85: PHY

## Slide 86: Topics in PHY
Data Rates
Modulations & Coding
OFDM
MIMO

## Slide 87: PHY Frame Structure (2.4 GHz)

## Slide 88: Data Rate & Modulation – 802.11 a/b/g

## Slide 89: Data Rate & Modulation – 802.11 n, 1x1:1

## Slide 90: Data Rate & Modulation – 802.11 n, 2x2:2

## Slide 91: BPSK

## Slide 92: QPSK

## Slide 93: OFDM - Multiplexing

## Slide 94: OFDM - Modulation

## Slide 95: MIMO - Spatial Streams

## Slide 96: RF

## Slide 97: 2.4 GHz Channels

## Slide 98: 5 GHz Channels
US: DFS required in 5470-5725 MHz U-NII band
US: DFS required in 5260-5320 MHz band

## Slide 99: Case studies

## Slide 100: Case 1: Dalian Hotel
File: case-DalianHotel.pcap
Observation
  At 7AM, there are no data traffic.
Questions
  On which channel was this captured?
  How many APs are there?
  Which are not protected?
Notes: 2.4GHz , Channel 1
2) & 3)
18:b0 – “Intercontinental” (open)– missed a lot of Beacons
18:b1 – “manager” (secured) – MAC is right after “Intercontinental”. Perhaps the same physical AP. Notice sequence number is in-sync with “Intercontinental”
2a:d0 – “Intercontinental” (open)
2a:d1 – “manager” (secured)

## Slide 101: Case 2: Beijing Airport
File: case-BeijingAirport.pcap
Observation
  There are quite a few APs.
Questions
  On which channel was this captured?
  How many APs are there?
  Which are not protected?
  Are there APs with the same SSID?

## Slide 102: Case 3: ARP
File: case-ARP.pcap
Observation
  Packets #1 and #3 are both broadcast packets.
Questions
  Why is #1 acknowledged?
  Why is #3 not acknowledged?

## Slide 103: Case 4: Deauth
File: case-Deauth.pcap
Observation
  DUT failed to connect.
Questions
  Was association successful at some point?
  When was DUT rejected?
  Why was it rejected?

## Slide 104: Case 5: Ping
File: case-Ping.pcap
Observation
  192.168.2.104 pings 192.168.2.111.
Questions
  Which one is a wireless station?
  How many ping requests were not answered?
  How many packets will be reported as “loss” by the PING app on 192.168.2.104?
  Why were they lost?